## Slide 2: Parallel Circuit
V
I1
I2
I
A
B

## Slide 3: Parallel Circuit
V
I1
I2
I
A
B

## Slide 4
V=12.0V
V=4.0V
8.0
1.0
1.0
3.0
5.0
I1
I3
I2

## Slide 5
V=12.0V
V=4.0V
8.0
1.0
1.0
3.0
5.0
I1
I3
I2

## Slide 6
V=12.0V
V=4.0V
8.0
1.0
1.0
3.0
5.0
I1
I3
I2

## Slide 7: Sources of emf
The source that maintains the current in a closed circuit is called a source of emf
  Any devices that increase the potential energy of charges circulating in circuits are sources of emf
  Examples include batteries and generators
SI units are Volts
  The emf is the work done per unit charge

## Slide 8: emf and Internal Resistance
A real battery has some internal resistance
Therefore, the terminal voltage is not equal to the emf

## Slide 9: More About Internal Resistance
The schematic shows the internal resistance, r
The terminal voltage is ΔV = Vb-Va
ΔV = ε – Ir
For the entire circuit, ε = IR + Ir

## Slide 10: Internal Resistance and emf, cont
ε is equal to the terminal voltage when the current is zero
  Also called the open-circuit voltage
R is called the load resistance
The current depends on both the resistance external to the battery and the internal resistance

## Slide 11: Internal Resistance and emf, final
When R >> r, r can be ignored
  Generally assumed in problems
Power relationship
  I e = I2 R + I2 r
    When R >> r, most of the power delivered by the battery is transferred to the load resistor

## Slide 12: RC Circuit
V
C
R
S

## Slide 13: RC Circuits
A direct current circuit may contain capacitors and resistors, the current will vary with time
When the circuit is completed, the capacitor starts to charge
The capacitor continues to charge until it reaches its maximum charge (Q = Cε)
Once the capacitor is fully charged, the current in the circuit is zero

## Slide 14: Charging Capacitor in an RC Circuit
The charge on the capacitor varies with time
  q = Q(1 – e-t/RC)
  The time constant, =RC
The time constant represents the time required for the charge to increase from zero to 63.2% of its maximum

## Slide 15: Notes on Time Constant
In a circuit with a large time constant, the capacitor charges very slowly
The capacitor charges very quickly if there is a small time constant
After t = 10 t, the capacitor is over 99.99% charged

## Slide 16: Discharging Capacitor in an RC Circuit
When a charged capacitor is placed in the circuit, it can be discharged
  q = Qe-t/RC
The charge decreases exponentially
At t =  = RC, the charge decreases to 0.368 Qmax
  In other words, in one time constant, the capacitor loses 63.2% of its initial charge

## Slide 17: Household Circuits
120V
Ground 0V
Meter
Circuit Breaker
Individual house appliances
Individual house switches

## Slide 18: Household Circuits, cont.
A meter and a circuit breaker are connected in series with the wire entering the house
Wires and circuit breakers are selected to meet the demands of the circuit
If the current exceeds the rating of the circuit breaker, the breaker acts as a switch and opens the circuit
Household circuits actually use alternating current and voltage

## Slide 19: Electrical Safety
Electric shock can result in fatal burns
Electric shock can cause the muscles of vital organs (such as the heart) to malfunction
The degree of damage depends on
  the magnitude of the current
  the length of time it acts
  the part of the body through which it passes

## Slide 20: Effects of Various Currents
5 mA or less
  Can cause a sensation of shock
  Generally little or no damage
10 mA
  Hand muscles contract
  May be unable to let go a of live wire
100 mA
  If passes through the body for just a few seconds, can be fatal

## Slide 21: Ground Wire
Electrical equipment manufacturers use electrical cords that have a third wire, called a case ground
Prevents shocks

## Slide 22: Ground Fault Interrupts (GFI)
Special power outlets
Used in hazardous areas
Designed to protect people from electrical shock
Senses currents (of about 5 mA or greater) leaking to ground
Shuts off the current when above this level

## Slide 23: Electrical Signals in Neurons
Specialized cells in the body, called neurons, form a complex network that receives, processes, and transmits information from one part of the body to another
Three classes of neurons
  Sensory neurons
    Receive stimuli from sensory organs that monitor the external and internal environment of the body
  Motor neurons
    Carry messages that control the muscle cells
  Interneurons
    Transmit information from one neuron to another

## Slide 24: Series Fluid Analogy
Upper Tank
Lower Tank
Middle Collection Tank
Pump
U1
U
U2

## Slide 25: Series Fluid Analogy
Upper Tank
Lower Tank
Middle Collection Tank
Pump
U1
U
U2
Flow meter

## Slide 26: Meters

## Slide 27: Series Fluid Analogy
Upper Tank
Lower Tank
Middle Collection Tank
Pump
U1
U
U2

## Slide 28: Meters

## Slide 29: Diagram of a Neuron

## Slide 30: Axons
From James E. Zull, The Art of Changing the Brain, Stylus, Sterling Virginia, 2002

## Slide 31: Signal Propagation
From James E. Zull, The Art of Changing the Brain, Stylus, Sterling Virginia, 2002

## Slide 32
E
r
R